## Slide 1: Welcome to ENEE244-02xx Digital Logic Design
Instructor: Dana Dachman-Soled
TA: Nathan Sesto
UTFs: Max DePalma (201,202)
Jordan Appler (203,204)

## Slide 2: Administrative Stuff
How to reach me:
  Email: danadach@ece.umd.edu
  Office: AVW 3407
Grading:
  Homework: 10%, Small quizzes: 6%,
  3 midterms: 54%, Final exam: 30%.
For detailed information see syllabus. Feel free to contact me with any questions.

## Slide 3: What is this course about?
Given a Boolean function , design a circuit computing
  Given only a truth table for
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
There are many ways of expressing this function.

## Slide 4: What is this course about?
Given a Boolean function , design a circuit computing
  Given only a truth table for
  Study techniques for finding the minimal circuit computing
Understand the design of basic circuit components
  Adders, comparators, decoders, encoders, multiplexers

## Slide 5: What is this course about?
Previous topics were all examples of combinational networks.
  Output depends only on the inputs at that instant.
Sequential networks
  Output depends on the state of memory
  Flip-flops—basic logic element of sequential networks
  Synchronous sequential networks—behavior determined by a clock signal

## Slide 6: List of Topics
Number systems
Boolean algebra
Combinational networks
  Design
  Analysis
Synchronous sequential networks
  Design
  Analysis

## Slide 7: Introduction

## Slide 8: Digital vs. Analog
Two general ways to represent information
  Digital: information is denoted by a finite sequence of digits. This form is discrete.
  Analog: a continuum is used to denote the information.
Examples:
  Digital vs. analog watch (range of angular displacement)

## Slide 9: Digital vs. Analog
Digital | Analog
Any degree of precision is possible by using more digits. | Measure to read information, precision is the number of digits obtained. Limitation on precision.
Can copy without degradation. e.g. digital recording. | Copying causes degradation. e.g. analog tape.
Groups of numbers can be compressed by finding patterns. Easy to manipulate. | Harder to compress and manipulate.

## Slide 10: Digital Computers
The electrical values (i.e. voltages) of signals in a circuit are treated as integers (0 and 1)
Alternative is analog, where electrical values are treated as real numbers.
Usually assume only use two voltages: high and low (square wave).
  Signal at high voltage: “1”, “true”, “set”, “asserted”
  Signal at low voltage: “0”, “false”, “unset”, “deasserted”
Assumption hides a lot of engineering.

## Slide 11: Representing Data Digitally

## Slide 12: Positional Number Systems
The decimal number system:
In general, can consider base r representation
We will be mainly concerned with the binary number system.
  Two digit symbols: 0,1
  A digit is referred to as a bit

## Slide 13: Positional Number Systems
Binary, Decimal, Hexadecimal
Hexadecimal:
  Base 16 (r = 16)
  Digit symbols: 0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F

## Slide 14: Basic Arithmetic Operations—Examples
Addition:
101100011 + 100110010
Subtraction:
101100011 – 100110010
Multiplication:
  1011 X 1001
Division:
100100/1100

## Slide 15: Switching Bases

## Slide 16: Algorithmic techniques
There are many ways to convert bases, e.g., can eyeball it.
Outline two algorithmic approaches to converting bases.
Can both be straightfowardly implemented on a computer.

## Slide 17: Polynomial method of number conversion
Convert from base to base
Express number as polynomial in base
Switch each digit symbol to its base representation and each base symbol to its base representation.
Evaluate the polynomial in base

## Slide 18: Polynomial Method of Number Conversion
Example: convert from hexadecimal to decimal
Hexadecimal number: A78E
Used when converting a number into decimal form.

## Slide 19: Iterative Method of Number Conversion
Convert from base to base .
Perform repeated division by . The remainder is the digit of the base number.
Example: Convert 50 from decimal to binary
  Divide 50 by 2, get 25 remainder 0
  Divide 25 by 2, get 12 remainder 1
  Divide 12 by 2, get 6 remainder 0
  Divide 6 by 2, get 3 remainder 0
  Divide 3 by 2, get 1 remainder 1
  Divide 1 by 2, get 0 remainder 1
Answer is: 110010
Can verify using the polynomial method
Used when converting from decimal to another base.

## Slide 20: Iterative Method for Converting Fractions
Convert from base to base .
Perform repeated multiplication by . The integer part is the digit of the base number.
Ex: Convert .40625 from decimal to binary
  Multiply .40625 by 2, get 0 + .8125
  Multiply .8125 by 2, get 1 + .625
  Multiply .625 by 2, get 1 + .25
  Multiply .25 by 2, get 0 + .5
  Multiply .5 by 2, get 1 + 0
Answer is: .01101
Can verify using the polynomial method

## Slide 21: Special Conversion Procedures
When converting between two bases in which one base is a power of the other, conversion is simplified.
Ex: Convert from 1101 0110 1111 1001 from binary to hexadecimal:
  1101 = 13 = D
  0110 = 6
  1111 = 15 = F
  1001 = 9
Answer: D6F9