## Slide 1: Equivalent Transformations Part 1: Series and Parallel Connections
ENEE 205

## Slide 2: EQUIVALENT TRANSFORMATIONS AND INPUT IMPEDANCE
Consider the two sub-circuits shown to the right. One circuit is said to be an equivalent transformation of the other if the relation between the voltage across the two terminals to the current entering the corresponding terminal is the same for the two sub-circuits.
Claim: If a sub-circuit is comprised of only linear, passive components, that sub-circuit can be replaced under sinusoidal steady-state conditions by a single passive branch.
If the replacement is done across the input terminals of the sub-circuit, the equivalent impedance is called the input impedance.

## Slide 3: Series connections of passive components
k components are said to be connected in series if they are all connected together by trivial nodes. Thus, they always share the same current!
KVL around the loop: =0
KCLs:
Inserting Impedances:
Or
Or a single impedance would have
Zeq so Zeq = Z1 + Z2 + …+Zj +…+ Zk

## Slide 4: Series connection examples
Impedances add in series: Zeq = Z1 + Z2 + Z3 +…+ Zk
Resistances add in series:
Inductances add in series
Voltage sources add in series

## Slide 5: Parallel connections of passive components
k components are said to be connected in parallel if they are all connected together by trivial meshes. Thus, they always share the same voltage!
KCL at lower node: =0
KVLs:
Inserting Admittances:
Or
Or a single admittance would have
Yeq so Yeq = Y1 + Y2 + …+Yj +…+ Yk

## Slide 6: Parallel connection examples
Admittances add in parallel : Yeq = Y1 + Y2 + Y3 +…+ Yk
Conductances add in parallel
Capacitances add in parallel
Current sources add in parallel
Ieq=30 mA
10 mA
10 mA
10 mA

## Slide 7: An R-2R ladder example

## Slide 8: Equivalent Transformations Part 2: Voltage and Current Divider Rules
ENEE 205

## Slide 9: VOLTAGE DIVIDER RULE
KVL around the loop: =0
KCLs:
Inserting Impedances:
Or
Since ,
Defining ,

## Slide 10: VOLTAGE DIVIDER RULE analysis
+
Vout
-
5000
V(t)=100cos(2t) V
2
2j
-j
-
-
-

## Slide 11: CURRENT DIVIDER RULE
KCL at lower node: =0
KVLs:
Inserting Admittances:
Or
S, so
Defining ,

## Slide 12: Current DIVIDER RULE analysis
Iin
Iout
So
i(t)=100cos(2t) mA
2j
-j/2
Iout
Iin
So

## Slide 13: Equivalent Transformations Part 3: Voltage and Current Divider Designs
ENEE 205

## Slide 14: Voltage divider DESIGN example
Design a resistive voltage divider with a ratio of 1:1000 (output : input) and an input impedance of 1 MW.
So
+
Vin
-
+
Vout
-

## Slide 15: Voltage divider DESIGN example
Design a capacitive voltage divider with a ratio of 1:10000 (output : input) and an input impedance magnitude of 50 W. The frequency is f = 100,000 Hz.
+
Vin
-
+
Vout
-

## Slide 16: Current divider DESIGN example
Design a resistive current divider with a ratio of 1:100 (output : input) and an input impedance of 100 W.
R1
R2

## Slide 17: Equivalent Transformations Part 4: The Superposition Principle
ENEE 205

## Slide 18: SUPERPOSITION PRINCIPLE
SUPERPOSITION ALGORITHM
Start with a circuit that contains M sources.
Divide the circuit into N sub-problems (often N=M, but that is not a necessary requirement.)
Make sure each source is “on” in exactly one of the sub-problems
Solve each sub-problem for the desired voltages and currents.
Find the desired voltages and currents for the original problem by summing up the respective voltages and currents for each of the sub-problems.
If you change reference directions for any of the sub-problems (not recommended, but possible), take that into account when summing the sub-problem results.
NOTE: Superposition works because all the SSS equations are linear (no diodes!)

## Slide 19: Setting a source to zero
This is only done with independent sources. Dependent sources and passive components remain the same in each sub-problem.

## Slide 20: 3 bit D-to-A converter example

## Slide 21
Original problem
Case (2)
Case (0)
Case (1)
++

## Slide 22: Case (2)
R-2R ladder, so the equivalent resistance is 2R

## Slide 23: Case 2, continued
The two outer 2R resistors are in parallel. By symmetry, those two resistors must have the same current going through them, so the battery B2 must be supplying 2iout. Recognizing the current coming out of the source allows one to combine the two outer resistors. Then, by using Ohm’s Law:

## Slide 24: Case 2, the end
If one were to solve for the other two cases, one would find: and
So that
Which is an equation for a 3-bit Digital-to-Analog converter.

## Slide 25: Equivalent Transformations Part 5: Op-amp Circuits with multiple input sources
ENEE 205

## Slide 26: Inverting Summing Amplifier
-
+
Rf
R1
R2
Rk
…
+
V1
-
+
V2
-
+
Vk
-
+
Vout
-
One can use superposition here. Let V1 be on and all other sources off. Then R2 through Rk are connected between the inverting and non-inverting terminals, and so have no voltage across them.
-
+
Rf
R1
R2
Rk
+
V1
-
+
Vout
-
…
Thus R2 through Rk also have no current through them and they can be removed form the circuit. What remains is a simple inverting amplifier, so .

## Slide 27: Inverting summing amplifier
-
+
Rf
R1
R2
Rk
…
+
V2
-
+
Vout
-
For Case (2), only V2 is on and all other voltages sources are replaced by shorts. R1 and R3 – Rk have no current though them and can be removed. What remains is a simple inverting amplifier, so .
For each case, only one source will be on, and the final circuit will be a simple inverting amplifier. The topology of each case looks the same, with only the subscripts changed, thus, the original equation for the output voltage will be:
++…+

## Slide 28: Subtraction Circuit
-
+
Rf
Rin
Rin
+
V1
-
+
V2
-
+
Vout
-
Rf
One can use superposition here. Let V2 be on and V1 be off. Then Rf and Rin are in parallel and can be replaced with an equivalent resistor.
-
+
Rf
Rin
Rin
+
V2
-
+
Vout
-
Rf
Since I+ =0, the non-inverting terminal is at ground and we have an inverting amplifer.
Thus,
(2)

## Slide 29: Subtraction circuit, continued
-
+
Rf
Rin
Rin
+
V1
-
+
V+
-
+
Vout
-
Rf
Now, consider the second case when V1 is on and V2 is off. Since I+ =0, the circuit below looks like a voltage divider. Thus:
Rin
+
V1
-
+
V+
-
Rf
(1)

## Slide 30: Subtraction circuit, the end
Given, the circuit effectively is as shown to the right, and that configuration is a non-inverting amplifier:
So:
+
Or
-
+
Rf
Rin
+
V+
-
+
Vout
-
(1)