## Slide 1: Filters 1: Definitions
ENEE 205

## Slide 2: Filter Definitions
Filter Circuit - A circuit that conditions an input signal, usually by allowing only a range of frequencies to pass through the circuit to the output. The purpose of a filter is often to separate a desired signal from undesired signals (e.g. noise).
Normalized Filter Circuit - A circuit whose parameters are adjusted so that the corner frequency is 1 radian/sec and the output impedance is 1 W.
Passive Filter – filters constructed without op-amps.
Active Filter – filters constructed with op-amps.
Butterworth Filter - A type of filter that is "maximally flat", i.e. as many derivatives of the magnitude of the transfer function as possible are equal to zero at some frequency.

## Slide 3: Filter Classification
Band-Pass Filter - A circuit that allows a range of frequency signals to pass through a circuit but attenuates low and high frequency signals.
Low-Pass Filter - A circuit that allows low frequency signals to pass through a circuit with a fairly constant loss (or gain ) but attenuates high frequency signals.
High-Pass Filter - A circuit that allows high frequency signals to pass through a circuit but attenuates low frequency signals.
Band-Notch Filter - A circuit that rejects a range of frequency signals to a circuit but allows low and high frequency signals to pass through with a fairly constant gain.
We define
Band pass Low pass High pass Band notch

## Slide 4: More Filter Definitions
Passband - The range of frequencies that passes through a filter relatively unattenuated (or at least fairly uniformly attenuated).
Insertion loss – The amount of attenuation (in dB) in the passband. This is typically -6dB for passive filters, because the maximum output voltage is ½ the input voltage. Active filters may actually have insertion gain (or loss).
Corner Frequency - The frequency where the power in the output signal is 50% of the output power in the passband. This is also known as the 3dB frequency and the breakpoint frequency.
Roll Off - The rate (in dB/decade) that the power in a signal is attenuated outside of the passband as a function of frequency.

## Slide 5: Filters: Part 2: Bode Plots and Frequency Response
ENEE 205

## Slide 6: Example: a passive 2nd order low-pass filter The output voltage found with Nodal Analysis

## Slide 7: BODE PLOTS – approximate frequency response for our second-order low-pass filter
Chart: Bode Plot versus actual frequency plot
| 0.01 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.7 | 0.8 | 0.9 | 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.5 | 1.7 | 1.8 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1000
 | -6 | -6.0004 | -6.0069 | -6.035 | -6.1098 | -6.2633 | -6.9346 | -7.491 | -8.1909 | -9.0103 | -9.9166 | -10.8765 | -11.8615 | -13.8265 | -15.7091 | -16.6061 | -18.3045 | -30.0993 | -42.1247 | -54.1649 | -66.206 | -78.2472 | -90.2884 | -102.3296 | -114.3708 | -126
 | -6 | -6 | -6 | -46
Exact frequency response
Bode Approximation
Worst case: off from approximation by 3 dB

## Slide 8: Filters Part 3: passive filters
ENEE 205

## Slide 9: Passive 3rd order filters

## Slide 10: Passive 3rd order low-pass filter
Solved with Nodal Analysis to show that it is a Butterworth Filter.

## Slide 11: Filter frequency and load scaling
If the required load impedance is RL and the required corner frequency is wo, simply take any values of R, L, and C that you find in the normalized circuit and replace them withand , respectively, according to the following formulas:
For example, if we need a load impedance of 51 W and a corner frequency of 3.45 kHz for our 3rd-order low-pass filter, we would replace both resistances with 51 W and

## Slide 12: Filters Part 4: Active Filters
ENEE 205

## Slide 13: Active first order filters
For 1st order circuits there are only low-pass and high-pass filters.
Low pass inverting
Low pass non-inverting
High pass non-inverting

## Slide 14: Normalized Low-pass 2nd-order Multi-feedback (MFB)
As with Node potentials:
Or
Or
KCL node -:
Or
so
And /

## Slide 15: More general MFB 2nd order Low-pass filter

## Slide 16: How to make a 3rd-order Low-pass filter

## Slide 17: Active 2nd-order circuits –Sallen-Key

## Slide 19
Designing an active filter!