## Slide 1: First Order Transients Part 1: Circuits excited by initial conditions
ENEE 205

## Slide 2: TRANSIENT CLASSIFICATION
We divide transient problems in two ways:
  Are there sources present for t>0?
  How many energy-storage elements are in the circuit for t>0?
We will study four cases:
  First-order circuits excited only by initial conditions (only one L or C)
  First-order circuits excited by sources (and perhaps initial conditions)
  Second-order circuits excited only by initial conditions*
  Second-order circuits excited by sources (and perhaps initial conditions)*
We will make extensive use of transfer functions in the solution of transient problems!
*These topics will be in the next set of notes. Circuits have two energy storage elements (1 L & 1 C, or 2 L’s or 2 C’s)

## Slide 3: RL AND RC CIRCUITS EXCITED BY INITIAL CONDITIONS
ALGORITHM:
Get circuit.
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Write complete set of 1st-order differential equations (draw circuit for t>0).
Rearrange equations to get one equation for desired unknown (usually a capacitor voltage or inductor current, irrespective of ultimate goal).
Find characteristic equation and general homogeneous solution.
Plug in initial condition to get specific solution.

## Slide 4
RC example 1 – find the capacitor voltage
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Write complete set of 1st-order differential equations (draw circuit for t>0 and NOTE that the switch is open for t>0!).
  (t)
+
Vc
-
+
VR
-
ic
iR
t>0

## Slide 5: RC example one
Rearrange equations to get one equation for desired unknown (usually a capacitor voltage or inductor current, irrespective of ultimate goal).
; So =0
Find characteristic equation and general homogeneous solution.
One way of finding the characteristic equation is to assume the homogeneous solution (recall your differential equations class) has the form: and plug it into the diff. eq.
, so =0
Since neither A nor will generally be zero, we get the Characteristic Equation: =0, so and

## Slide 6: RC example one
The “,h” in the subscript denotes that this is the homogeneous solution, which is also the total solution when there are no sources in the circuit for t>0. The unknown amplitude A makes it a general solution, since A has yet to be determined.
We often define the time constant =RC so that we can write the solution as: . (Yes, RC has units of seconds)
Plug in initial condition to get specific solution.
So, the specific solution is for
Now we can find any voltage or current that we wish, for example, also

## Slide 7: RC example one

## Slide 8: RC example 2
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Because for steady-state, there can not be any current into the capacitor (since the source is DC)
Write complete set of 1st-order differential equations (draw circuit for t>0).
Because the circuit for t>0 for this problem is identical to the circuit for t>0 of the last problem, steps 3-5 give identical results and we are left with the general homogeneous solution:
+
Vc
-
+
VR
-
ic
iR
t>0
Plug in initial condition to get specific solution.
So, the specific solution is for

## Slide 9: RL example – find the inductor current
Find initial condition on energy storage element (is DC, so all current goes through the inductor).
Write complete set of 1st-order differential equations (draw circuit for t>0).
  (t)
+
VL
-
+
VR
-
iL
iR
t>0

## Slide 10: RL example one
Rearrange equations to get one equation for desired unknown (usually a capacitor voltage or inductor current, irrespective of ultimate goal).
; So =0
Find characteristic equation and general homogeneous solution.
A and plug it into the diff. eq.:
, so =0
Since neither A nor will generally be zero, we get the Characteristic Equation:=0, so and

## Slide 11: RL example one
Plug in initial condition to get specific solution.
So, the specific solution is for
Now we can find any voltage or current that we wish, for example,
Chart: Inductor Current vs time =10 s, Io = 5A
Note that , so jumped instantly at t=o! That is fine; only must be continuous to be consistent with our finite power assumption.

## Slide 12: RL example two
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Finding the initial conditions for us will always be a sinusoidal steady-state problem, because we assume that the circuit for t<0 was set up way in the distant past, so that any transients have died off. Since is , =0, the inductor as zero impedance (again, for t<0) and is divided between , thus, by the current divider rule:
+
VL
-
+
VR
-
iL
iR
t>0
L
The circuit for t>0 is shown on the right, since are in series after the switch opens. This is the same circuit as the previous case, so
for

## Slide 13: First Order Transients Part 2: Circuits excited by sources
ENEE 205

## Slide 14: CIRCUITS EXCITED BY SOURCES
ALGORITHM (Note that steps 1-5 are identical with last algorithm):
Get circuit.
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Write complete set of 1st-order differential equations (draw circuit for t>0 .)
Rearrange equations to get one equation for desired unknown (usually a capacitor voltage or inductor current, irrespective of ultimate goal)
Find characteristic equation and general homogeneous solution
Find the particular solution by method of undetermined coefficients or SSS analysis.
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution.

## Slide 15: RC Circuits excited by sources
  Find the voltage across the capacitor for t>0.
Find initial condition on energy storage element (If no source for t<0, always assume zero!).
Write complete set of 1st-order differential equations (NOTE that the switch is closed for t>0!).
  (t)
- Vr +
ir
ic
+
Vc
-
+
300
-
Rearrange equations to get diff eq. for

## Slide 16: RC Circuits excited by sources
Find characteristic equation and general homogeneous solution. One needs to set the driving term to zero to do this:
Plugging in , we get =0
Or the same characteristic equation as for the RC circuit excited by initial conditions: =0
So
Find the particular solution by method of undetermined coefficients or SSS analysis.
Undetermined coefficients means that the particular solution follows the form of the driving term and we just need to find the right unknown coefficients by plugging into the diff. eq. Since the driving term is a constant, the particular solution is a constant:

## Slide 17: RC Circuits excited by sources
Thus, is for particular solution) and the differential equation for the particular solution is just
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution.
The complete solution is the sum of the homogeneous and particular parts:
The initial condition is:
So
So , and:

## Slide 18: RC Circuits excited by sources
Chart: Capacitor Voltage
=0.94 ms

## Slide 19: RC Circuits excited by sources
  Find the time T>0 when the voltage across the capacitor equals 0V. We have to follow the algorithm and use the answer to find the zero crossing!
Find initial condition on energy storage element. Here drawing the circuit for t<0 might be useful. A constant 50 A is to divide between the resistor and the capacitor, but because =0, the capacitor impedance is infinity and all 50 A goes through the resistor. Ohms Law tells use that the voltage is 100V as shown,
50 A
2 W
-
100V
+
+
Vc
-
t<0
So (Note polarity difference between resistor and capacitor).

## Slide 20: RC Circuits excited by sources
Write complete set of 1st-order differential equations. Draw the circuit for t>0.
2 W
2 W
1 mF
- 200 V +
It would be easier to solve for if we convert the non-ideal voltage source into a non-ideal current source. We could then combine the two resistors that would be in parallel into a single 1W resistor.
KCL for bottom node:
KVL for left mesh:
Terminal relations: ;
Plugging TRs and KVL into KCL yields:
1 W
1 mF
100 A
- Vc +
- VR +
iR
iC
(Step 4 was combined in the process)

## Slide 21: RC Circuits excited by sources
Find characteristic equation and general homogeneous solution. One needs to set the driving term to zero to do this: for , we get:
Or or = 1W times 1 mF = 1 ms.
In fact, for any 1st order transient problem with a capacitor, the time constant will always be some equivalent resistance times the capacitance C. If there are more than one resistor, the only “trick” is to determine the equivalent resistance and then one can write the homogeneous equation “by inspection.”
Find the particular solution.
Since the driving term is a constant, , and the diff. eq. says: so : and
Or

## Slide 22: RC Circuits excited by sources
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution.
The complete solution is the sum of the homogeneous and particular parts:
The initial condition is:
So
So , and:
Now or
Or or

## Slide 23: RL Circuits excited by sources
  Find the current through the inductor for t>0.
Find initial condition on energy storage element (If no source for t<0, always assume zero!).
Write complete set of 1st-order differential equations. Draw the circuit for t>0. 4. Rearrange equations to get diff eq. for
KCL: KVL:
(t)
Plug TRs and KCL into KVL:
L
R
+
Vo
-
iL
iR
- vR +
+
vL
-
Find characteristic equation and general homogeneous solution.
;

## Slide 24: RL Circuits excited by sources
Or for
In fact, for any 1st order transient problem with an inductor, the time constant will always be some inductance L divided by the equivalent resistance . If there are more than one resistor, the only “trick” is to determine the equivalent resistance and then one can write the homogeneous equation “by inspection.”
Find the particular solution.
Since the driving term is a constant, , and the diff. eq. says: so : /R and
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution
So and for

## Slide 25: RL example: Vo=150V, R = W, L=470 mH
Chart: Inductor current (A)
=0.94 ms

## Slide 26: RL Circuits excited by sources
  Find the voltage across R2 for t>0. Note: find inductor current first!
Find initial condition on energy storage element (If no source for t<0, always assume zero!).
KCL: KVL:
(t)
Plug TRs & KVL into KCL:
Write complete set of 1st-order differential equations. Draw the circuit for t>0. 4. Rearrange equations to get diff eq. for It is useful, but not essential, to recognize that does not affect or - it only affects the voltage across .and so can be replaced with the Norton Equivalent source, which is just the ideal
R2
L
Io
- VL +
- VR +
iR
iL

## Slide 27: RL Circuits excited by sources
Find characteristic equation and general homogeneous solution.
;
Find the particular solution.
Since the driving term is a constant, , and the diff. eq. says: and
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution
So and for

## Slide 28: First Order Transients Part 3: Transfer functions in transient problems
ENEE 205

## Slide 29: Transfer functions in transient problems
Why might transfer functions be useful for the solution of transient problems?
When the source is sinusoidal (for t>0), the particular solution to the problem is the sinusoidal, steady-state solution, which can be found via transfer functions.
The general homogeneous solution can always be found from the transfer function (for concreteness assume input and output signals are voltages):
So, the only way to have a non-zero solution for the desired voltage or current when the source is equal to zero, is to have the transfer function go to infinity, which is to say “s” must be a pole of the transfer function, or that the characteristic equation for the circuit can be found by setting the denominator of the transfer function equal to zero.

## Slide 30: SOLVING 1st-ORDER PROBLEMS WITH TRANSFER FUNCTIONS
ALGORITHM (circuits excited by sinusoidal sources):
Get circuit.
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Find transfer function of desired output in terms of source (draw circuit for t>0 .)
Find characteristic equation by setting denominator of transfer function to zero. Obtain general homogeneous solution.
Find the particular solution by inserting s=jw into transfer function and solving.
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution

## Slide 31: Find the current through the inductor for t>0.
Solving first-order problems with transfer functions
Find initial condition on energy storage element (If no source for t<0, always assume zero!).
Find transfer function of desired output in terms of source (draw circuit for t>0 .)
Io
- VL +
- VR +
iR
iL
Use the current divider rule to get the transfer function:
Or
Find characteristic equation by setting denominator of transfer function to zero. Obtain general homogeneous solution.
or and

## Slide 32: Solving first-order problems with transfer functions
Find the particular solution by inserting s=jw into transfer function and solving.
So A
Plug in initial condition to COMPLETE solution (general homogeneous plus particular) to get specific solution
Or or

## Slide 33: TRANSFER FUNCTION EXAMPLES FOR CIRCUITS EXCITED ONLY BY INITIAL CONDITIONS
ALGORITHM (circuits excited by initial conditions):
Get circuit.
Find initial condition on energy storage element (draw circuit for t<0 if needed).
Add a source to the circuit so that you recover the original circuit when you set the source to zero!
Find transfer function of desired output in terms of source (draw circuit for t>0 .)
Find characteristic equation by setting denominator of transfer function to zero. Obtain general homogeneous solution.
Plug in initial condition to the general homogeneous solution to get specific solution. (The particular solution is zero.)

## Slide 34: Method 1 – add a voltage source
  Find the voltage across the capacitor for t>0.
We’ll only concentrate on the step where we add the fictitious source. For t>0 the circuit looks like this on the right.
-
Vc
+
+
VR
-
ic
iR
t>0
R
-
Vc
+
+
VR
-
ic
iR
t>0
R
+ Vo -
We add a series voltage source as shown on the left. If the source is set to zero, we recover the circuit on the right.
We use the voltage divider rule to get: . We only care about the denominator to get the Characteristic equation: =0, so

## Slide 35: Method 2 – add a current source
  Find the voltage across the capacitor for t>0.
We’ll only concentrate on the step where we add the fictitious source. For t>0 the circuit looks like this on the right.
-
Vc
+
+
VR
-
ic
iR
t>0
R
We add a parallel current source as shown on the left. If the source is set to zero, we recover the circuit on the right.
-
Vc
+
+
VR
-
ic
iR
t>0
sC
Io
We use the current divider rule to get: . We want , and , so: or . We care about the Characteristic equation: =0, so